## Slide 1: Solar Panel Potential Energy
An analysis of solar array and weather data from 2015-2017
Analysis Team
Elham Amini
Shikhar Bahadur Bhandari
JP Burgess
Tyler Lentini
Stan Misina
Tony Prahtchaya Poonsombaht

## Slide 2: Project purpose
Our team has collected insight to power generation of deployed solar arrays – in this case the panels managed by NIST in the Washington DC metro area.
Our intention is to present energy generation insight that will anticipate output for future project deployment considering several correlated conditions.
Understanding the predictability and efficiency of solar panel arrays will encourage increased implementation and future research.

## Slide 3: Data sources implemented
NIST Photovoltaic Array Database - https://pvdata.nist.gov/
  Features: A database covering minute to minute solar panel output and from 2015 to 2017.
Weather data from NREL: https://developer.nrel.gov/
  The API includes access to an extensive array of features in a large databases. For this project, we selected those applicable to solar data.

## Slide 4: Preliminary Questions
Can data analysis be used to more clearly anticipate the power generation of solar arrays?
Is there a particular set of conditions (features) that impacts panel output?
Initial MLM Question: Can we predict the output of a solar panel array based on weather data?

## Slide 5: Preliminary Questions
Hypothesis: There is a statistically significant correlation between solar panel output and weather data.
Null Hypothesis: There is not a statistically significant correlation between solar panel output and weather data.

## Slide 6: Data Exploration: Data Cleaning
Cleaning the data meant inspecting for null values, converting measures and preparing databases to be merged together.
We have joined tables and created two new tables consisting of data united by time stamp information.
We investigated outliers and relevant data; therefore, it was determined to drop data points where panels were not generating at least 30 volts of energy. This removes nighttime hours and anomalous negative data points from observed output.

## Slide 7: Data Exploration: Database
Our table schemas evolved throughout data exploration to find the most impactful information effecting solar power.
The first version of our DB included all the columns; however, loading features key for visualization and our machine learning model (MLM) weren’t addressed as we further investigated the data.
Later iterations, including the model presented here, take in all the data focused on key features (solar_data_v2).

## Slide 8: Data Exploration: Array Locations
Systems:
Parking Lot Canopy Array 1032 modules with a rated DC output of 243 kW.
Ground Mount Array 1152 modules with a rated DC output of 271 kW.
Roof Tilted Array 312 modules with a rated DC output of 73.3 kW

## Slide 9: Analysis: Negative DC input
InvVDCin_avg = average direct current generated (“Voltage Output”)
In exploration and processing, we observed negative values in Voltage Output. As a solar cell would generate energy – not consume it, these anomalies are excluded.
The negative results are accounted as a result of maintenance, animal interference, management system testing, upgrades, and adding or replacing panels among others.

## Slide 10: Analysis: Panel Tilt and Input
Of the three tilt angles and locations, ground at 20 degrees, canopy at 10 degrees, roof at 5 degrees -- ground has proved to be the least productive for Voltage Output.
Although this observation is true, the relationship between tilt angle and Voltage Output cannot be sufficiently tested by this data set.
As the tilt is singularly fixed at each position, a comparative analysis of the different tilts is not possible.

## Slide 11: Analysis: DHI, DNI, and GHI
Direct Normal Irradiance (DNI) - Think direct sunlight
Diffuse Horizontal Irradiance (DHI) - ambient sunlight
Global Horizontal Irradiance (GHI) - an accumulative calculation of the DNI and DHI

## Slide 12: Technology, Languages, Tools and Algorithms:
Technology/Tools: Pandas, Excel, CSS, Tableau, Web scraping w/ Python, SqlAlchemy, Jupyter Notebooks
Languages: Python, JavaScript, HTML, SQL
Algorithms: Neural Network, Random Forest, Linear Regression